## Slide 1
UTM
Universiti Teknologi Malaysia
A Concurrent Real-Time Control System
for Autonomous Vehicle Simulation
Using Rate Monotonic Scheduling
Umayra | Adam | Aisyah | Nopal
Faculty of Computing • Universiti Teknologi Malaysia • 2026
Notes: Welcome. Today we present our RTSE group project.

## Slide 2
UTM
Presentation Outline
01
Introduction & Problem Statement
What is real-time software engineering? Why does timing matter for autonomous vehicles?
02
Background Study
Concurrent programming, RMS scheduling, µC/OS-II, SpeedTrials2D simulation environment
03
System Design & Implementation
8-task RMS architecture, scheduling table, schedulability analysis
04
Case Study: AutoRS Comparison
AutoRS framework, scheduling review, benchmarking against our system
05
Redesign & Real-World Proposal
Sensor stack scaling (LiDAR/Radar), optimisation, WCET/HiL validation

## Slide 3
UTM
01 Introduction

## Slide 4
UTM
What is Real-Time Software Engineering?
Definition
A discipline where correctness depends on BOTH the logical result AND the time of delivery.
A late result is treated as a wrong result.
Hard vs Soft Real-Time
Hard RT: Missing a deadline = system failure Example: AV collision avoidance Soft RT: Missing a deadline = degraded quality
Example: video streaming buffering
Problem Statement
In a dynamic track with lane changes, token collection, and unpredictable hazard events, the autonomous vehicle must complete a full sense–decide–actuate cycle within a reaction window that shrinks as speed increases.
A missed deadline on the perception or steering task does not degrade gradually — it causes a control error that compounds across cycles, ultimately leading to lateral instability or collision.

## Slide 5
UTM
Project Goal & Contributions
Goal: Develop a concurrent, multi-threaded Python controller for SpeedTrials2D, modelled on µC/OS-II, using RMS to study how scheduling policy and priority assignment affect vehicle stability.
(i)
Concurrent Controller
8 periodic tasks with mutex-protected shared state, emulating µC/OS-II preemptive kernel
(ii)
Schedulability Analysis
RMS utilisation bound + response-time analysis to formally verify all task deadlines are met
(iii)
AutoRS Benchmark
Compare fixed-priority static design against AutoRS adaptive industrial-grade scheduler
(iv)
Redesign Proposal
Identify task period and priority changes for higher speeds and LiDAR/Radar sensor fusion

## Slide 6
UTM
02 Background Study

## Slide 7
UTM
Concurrent Programming
Why Concurrency?
A single sequential loop is too slow.
Each stage must progress independently so no one stage stalls the others.
Concurrent tasks keep each stage latency bounded and independent.
Hazards & Remedies
Race Condition
→ Mutex: only one task enters critical section at a time
Priority Inversion
→ Priority Inheritance Protocol (Sha et al., 1990): temporarily elevates lock-holder's priority so it can finish and release the mutex quickly
Perceive – Compute – Actuate Pipeline (PCA)
PERCEIVE
Camera frames
(OpenCV/HSV)
→
COMPUTE
Lane scoring
& decision
→
ACTUATE
Steering &
throttle output

## Slide 8
UTM
Real-Time Scheduling Fundamentals
Periodic Task Model: each task τᵢ has Period (T) · WCET (C) · Deadline (D) | Utilisation Uᵢ = C / T
Rate Monotonic
Scheduling (RMS)
Fixed priority — shorter period = higher priority
Proven optimal among all fixed-priority algorithms
Liu & Layland bound: U ≤ n(2^(1/n)−1) → ≈ 69.3% for large n
Predictable and analytically tractable
Earliest Deadline
First (EDF)
Dynamic priority — nearest deadline = highest
Theoretically optimal: can use 100% CPU
Harder to predict under overload conditions
Cascading deadline misses when overloaded
Response-Time
Analysis (RTA)
Tighter schedulability test than utilisation bound
Rᵢ = Cᵢ + Σⱼ<ᵢ ⌈Rᵢ/Tⱼ⌉·Cⱼ (iterate to fixed point)
Schedulable if Rᵢ ≤ Tᵢ for all tasks
Used to formally prove our design is safe

## Slide 9
UTM
µC/OS-II Modelling & SpeedTrials2D
µC/OS-II
Preemptive, priority-based RTOS kernel Key features: • Highest-priority task always runs first • Mutexes with Priority Inheritance • Message queues for inter-task comms • Bounded blocking semantics Python emulation: RTTask → threading.Thread
shared_data → global dict
data_lock → threading.Lock
Period → time.perf_counter sleep
SpeedTrials2D (V3)
Unity 2D racing simulation 5-lane road • OpenCV vision • TCP socket 5 Events (rotate every 60s): EV1 Darkness → send accel = −1.0 EV2 Police Car → collect red token in 5s EV3/4 Chasing Car → avoid collision EV5 Golden Lane → be in lane at expiry Tactical Win Condition: Net +60 green tokens AND pass all events at least once

## Slide 10
UTM
03 System Design &
Implementation

## Slide 11
UTM
Concurrent Task Architecture — RMS Schedule
8 Periodic Tasks — shorter period → higher priority (Rate Monotonic Rule)
Task
Role
Period
Priority
WCET
Util.
Note
SendControls
Actuation
2 ms
HIGH
0.5 ms
0.250
Always sends latest control
ReadFrontCamera
Perception
5 ms
HIGH
1.5 ms
0.300
Feeds brightness + detection
BrightnessTask
Perception
5 ms
HIGH
0.5 ms
0.100
Challenge 1: low light
DecisionTask
Compute
5 ms
HIGH
1.0 ms
0.200
Lane scoring state machine
ReadBackCamera
Perception
10 ms
MED
1.5 ms
0.150
Chasing car feed
DetectionTask
Compute
10 ms
MED
5.0 ms
0.500
Coins + police + chasing + HUD
PoliceWatchdog
Compute
100 ms
LOW
0.3 ms
0.003
Police deadline countdown
GoldenLaneWatchdog
Compute
100 ms
LOW
0.3 ms
0.003
Golden lane timer + tactical win
Total Utilisation
1.508 (distributed across multi-core PC)

## Slide 12
UTM
Schedulability Analysis
RMS Utilisation Bound
For n=8 tasks:
U ≤ 8(2^(1/8)−1) ≈ 69.4%
Tasks grouped by priority level:
HIGH group: 4 tasks, 2–5ms periods
MEDIUM group: 2 tasks, 10ms periods
LOW group: 2 tasks, 100ms periods
Each group schedulable within its processor core.
Response-Time Analysis
Rᵢ = Cᵢ + Σⱼ<ᵢ ⌈Rᵢ/Tⱼ⌉·Cⱼ
(iterate until fixed point)
All tasks verified:
SendControls: R ≈ 0.5ms < 2ms ✓
ReadFrontCam: R ≈ 2.0ms < 5ms ✓
DetectionTask: R ≈ 8.5ms < 10ms ✓
PoliceWatchdog: R ≈ 6.8ms < 100ms ✓
Key Design Decisions
SendControls at 2ms = HIGHEST priority
→ Actuation thread always gets CPU first
DecisionTask at 5ms
→ Interprets latest sensor data
→ Computes steering & throttle
DetectionTask at 10ms MEDIUM
→ Heavy OpenCV processing
→ Never blocks the control path

## Slide 13
UTM
04 Case Study:
AutoRS Comparison

## Slide 14
UTM
AutoRS: Environment-Dependent Real-Time Scheduling
Ma, Li & Xu — IEEE Trans. Parallel Distrib. Syst., Vol. 34, No. 12, Dec. 2023 | University of Macau
The Problem
AV task execution time varies with environment:
• Sensor fusion: 20ms → 40ms as traffic density rises
• Object detection: 70ms → 170ms in complex scenes
With static scheduling, increased execution causes cascading deadline misses for all downstream tasks.
Result: control commands delayed → vehicle cannot update speed → collision risk.
AutoRS Solution
Inner Control Loop
Environment Guided Controller
Calculates tracking error E(t).
Adjusts priority coefficient γ:
→ High error: prioritise control chain (responsive)
→ Low error: prioritise deadline-first (throughput)
Outer Control Loop
RL-based Task Rate Coordinator
Markov Decision Process.
Monitors CPU load + deadline miss ratio.
Dynamically adjusts sensor task release rates
to prevent overload or underutilisation.
Performance gain: 7.95% – 56.9% over static baselines

## Slide 15
UTM
Scheduling Review & Benchmarking
Dimension
SpeedTrials2D (RMS)
Pure EDF
AutoRS (Hybrid)
Priority assignment
Fixed (static RMS)
Dynamic (deadline)
Hybrid: γ × priority + deadline
CPU utilisation
≈69.3% bound
Up to 100%
Adaptive (RL-tuned rates)
Environment awareness
Event state machine
None
Tracking error E(t)
Overload behaviour
Predictable, bounded
Cascading misses
Outer loop reduces sensor rates
Implementation
Python threads + Lock
Theoretical
Nvidia Jetson TX2, 23 tasks
Performance gain
Simulation adequate
EDF baseline
Up to +56.9% vs Apollo
Both share the same Perceive–Compute–Actuate architecture. AutoRS dynamically adjusts γ every cycle based on real driving conditions; our system uses a manually coded event state machine as a fixed approximation of this concept.

## Slide 16
UTM
05 Redesign &
Real-World Proposal

## Slide 17
UTM
Redesign: Task Criticality & Sensor Pipeline
Task Criticality Groups
Safety-Critical Control
Steering, braking, emergency avoidance
Directly affects vehicle safety — always first
Perception & Fusion
Camera, LiDAR, Radar, object detection
Provides information — runs concurrently without blocking control
Support Tasks
Logging, visualisation, debug
Can be delayed or dropped under high CPU load
Proposed Sensor Pipeline
Camera + LiDAR + Radar
↓
Preprocessing
↓
Sensor Fusion
↓
Prediction
↓
Path Planning
↓
Steering / Braking Control

## Slide 18
UTM
Redesign: Schedulability Validation
Manual observation is not sufficient for a real vehicle — three formal validation methods required
WCET Benchmarking
Measure worst-case execution time of every task on actual embedded hardware.
• Log: release time, start, finish, execution time, blocking time, deadline misses
• Task schedulable only if worst-case response time ≤ deadline
• A task fast on laptop may be slow on vehicle controller
Hardware-in-the-Loop (HiL)
Run real controller on embedded hardware with simulated sensor inputs.
• Feed camera, LiDAR, Radar data into controller
• Check latency, CPU load, mutex blocking, contention
• Unsafe sign: control task delayed or misses deadline
• Also used by AutoRS to validate scheduling
Safety Threshold Analysis
Find operating limits by gradually increasing speed, density, sensor rate.
• Unsafe signs: missed steering/braking time, CPU > 85–90%, large lane deviation, low time-to-collision
• Determine safe envelope: e.g. stable at 30 km/h, unsafe at 40 km/h
• Fix: reduce non-critical sensor rates or enter safe mode

## Slide 19
UTM
Conclusion
01
Concurrent Controller Built
8 periodic RMS tasks with mutex-protected shared state, successfully mirroring µC/OS-II in Python.
02
Schedulability Verified
RMS utilisation bound and response-time analysis confirm all task deadlines are met under the assigned priority ordering.
03
AutoRS Benchmark
Static RMS is predictable and sufficient for simulation. AutoRS outperforms by up to 56.9% in complex environments because it adapts priorities in real time.
04
Redesign Proposal
LiDAR + Radar fusion, dynamic scheduling, WCET/HiL/safety-threshold validation needed to extend the design to a real autonomous vehicle.

## Slide 20
UTM
Thank You
Questions & Discussion
Umayra · Adam · Aisyah · Nopal Faculty of Computing
Universiti Teknologi Malaysia • 2026
References: [1] Ma et al. AutoRS, IEEE TPDS 2023 [7] Liu & Layland, J.ACM 1973 [8] Sha et al., IEEE Trans.Comput. 1990 [6] Labrosse, µC/OS-II 2002 [3] Kopetz, Real-Time Systems 2011